## Slide 1: Bioprocessing
The journey from milligrams to tonnes
Bob Holt
Notes: This presentation focuses on the processing constraints of operating on plant, how these differ to those encountered at laboratory scale and why it is important to understand these constraints before embarking on any scale-up work.
This presentation describes processes based on fermentation but many of the points discussed also relate to other processes, for example those using enzymes.

## Slide 2: Overview
Before you start
Process overview
Microbe selection
Fermentation Development
Product Recovery & Purification
Formulation
Logistics

## Slide 3: Will your process be cost competitive?
Bulk Prices
Don’t use catalogue prices
There is no “green premium”
Rough Estimate
Reasonable assumptions
Notes: There is almost always more than one way to solve a problem or make a product and in a free-market economy the cheapest process will always win (all other things being equal).
No matter how exciting or interesting your technology might be nobody will want to fund a process that converts gold into lead; it might win you a Nobel Prize, but it won’t make you rich.
It is essential to understand the market you are trying to address. What is the market price of the material you plan to make at bulk scale? This can be orders of magnitude lower than catalogue prices.
Take account of raw materials costs, process yields, plant operating (or toll manufacturing) costs and profit margin. Initially this will be a rough estimate, but it is an essential go/no go decision point.
An understanding of the breakdown of the process costs can also inform which areas to focus development on. Product concentration is a major factor influencing process cost and should always be a major point of focus.
It is important to remember that in most cases there is no “green premium” for products made by bioprocesses; everyone wants to be green, but nobody wants to pay for it. The few exceptions to this include cosmetics and some food products where marketing directly to end consumers plays a vital role.

## Slide 4
How will your process operate at scale?
Traditional scale up
Scale down
Laboratory
optimisation
Pilot
optimisation
Demonstration
optimisation
Fail-learn
Fail-learn
Fail-learn
Fail-learn
Fail-learn
Full scale
optimisation
Iterative
laboratory
optimisation
Optimised
process
Full scale
optimised
process
Notes:   A common mistake is to optimise a process under laboratory conditions using laboratory equipment, but the constraints of operating at large scale mean that different approaches must be taken and a direct scale-up of a laboratory process to a plant reactor is rarely possible.
  By understanding the constraints of plant operations at the forecast final production scale it is possible to evaluate a process under large-scale conditions but in small scale equipment – this is often referred to as the scale-down approach. By adopting this approach more experiments can be done at much lower cost; critical variables can be identified and safe operating windows scoped prior to commitment to expensive large-scale trials.
  By collecting data under scale-down conditions the risk of surprises, or even total failure, on scale-up are significantly reduced. Data from scale-down experiments can also be invaluable for refining the economic model.
  Consider applying the partial factorial approach to experiments to optimise conditions and identify any non-obvious interactions between variables.
  Image credit: iStock image - Stock illustration ID:2188346914

## Slide 5
General process development flow diagram
Biocatalyst screening.
Microbe or enzyme
Fermentation producing
a metabolite, enzyme
or biomass
Reaction optimisation
Product recovery
and purification
Formulated product
to end-user
Raw material
processing
Approach is the same
irrespective of final scale
Notes: Every process is different, so a generic process flow diagram has been used to illustrate the unit operations found in many bioprocesses.
The first step in most processes is the selection of the appropriate production organism or biocatalyst; this is one stage where the technical approach is the same whether the end goal is bench scale or large-scale operation. The rest of the steps are likely to differ in detail depending on the scale of operation.
Fermentation is often a key step whether it be to produce a natural product, an enzyme (both of which may be intra- or extracellular) or the biomass itself.
Product recovery, and potentially purification of the product are very important steps which often do not get the attention they require during the early stage of process evaluation and development.
Another issue which is often overlooked is the final form of the product.
Additional steps may include a biocatalytic reaction and pre-processing of raw materials.
Subsequent slides will address each of these (apart from raw material processing which is addressed elsewhere) in more detail.

## Slide 6: How do you select your microbe?
Antibiotic selection
Not practical at scale
Cost and disposal
May be ok during growth of inoculum
Avoid beta-lactams
ACDP groups
Prefer Group 1
Group 2 will require additional safety and regulatory controls
Additional cost
Notes: In any process involving microorganisms it is preferable to use those complying with biosafety level 1 containment requirements as defined by the Advisory Committee on Dangerous Pathogens (ACDP). Although biosafety level 2 organisms can be grown at scale this requires additional controls and regulatory approvals and many toll operators will not be willing to handle them.
In the laboratory, antibiotic selection is used routinely, primarily for selection of microorganisms expressing heterologous genes but this approach is rarely used at scale for reasons of cost and the requirement to irreversibly inactivate any antibiotic prior to discharge of waste to a treatment plant. The use of antibiotic selection during small scale growth of inoculum may be acceptable. In any case, beta-lactam antibiotics are best avoided completely due to the risk of allergic reaction/anaphylactic shock in sensitive people.

## Slide 7: Consider full-scale constraints from day 1
Key considerations
  The reactor:
    Oxygen consumption rate
    Heat removal rate
    Mixing times
Reproducibility: push operating boundaries on purpose
Consider partial factorial experiment design
Oxygen
Heat
Mixing times
Oxygen
Heat
Mixing times
Notes: Fermentation at large scale poses different constraints to those found in a typical laboratory fermenter.
Maximum aeration rates are likely to be no more than 1 volume per minute and the use of pure oxygen as a supplement is unlikely to be an option due to logistics, cost and safety concerns.
Whereas laboratory fermenters often require heating to maintain the desired temperature, in large scale fermenters it is usually necessary to cool the vessel due to the heat generated through metabolic activity and the energy input from the agitator. Heat removal capacity can limit the maximum achievable growth rate
Mixing times in large vessels are much longer than in small vessels and this can have an impact on feedback control of pH (amongst other things) leading to broader operating ranges compared to small scale laboratory vessels.
Image credit: Royalty free from Dreamstime

## Slide 8: Fermentation development
Medium composition
Keep it simple
Minimise use of complex components
Growth mode
Fed batch has many advantages
High cell density
Ability to control growth rate
Recombinant expression
Elimination of antibiotics
Inducer concentration
Induction timing
Keep it simple
Notes: Commonly used laboratory growth media such as Luria-Bertani and Terrific Broth are not typically used at large scale for several reasons including cost and the increased risk of foaming in the presence of high concentrations of complex medium components. Media should be as simple as possible and where complex components are required animal derived products should be avoided due to the perceived risk of transmissible spongiform encephalopathy.
Fed-batch is the most common mode of fermentation at industrial scale and has several advantages over a simple batch. High cell densities (30-50 grams dry weight per litre in bacterial cultures and even higher in Pichia cultures) can be achieved by feeding a carbon/energy source such as glucose or glycerol. In addition, the feed rate can be used to control growth rate which has the knock-on effect of controlling oxygen consumption rate and heat output rate.
At larger scale the use of IPTG as inducer can be a significant cost if used at 1.0 mM concentration as often used in the laboratory. In most cases a concentration of 0.1 mM or less will produce equivalent levels of expression. Lactose can also substitute for IPTG in glucose-limited fed-batch cultures. A further significant difference is that whereas in laboratory experiments it is typical to induce at very low cell density, in large scale E. coli fermentations induction is often carried out shortly before reaching maximum cell density. Genetic expression systems should be chosen on the basis of simplicity and robustness; for example, don’t use co-expressed chaperones if expression at a low temperature can achieve the same result. The more parts you have, the more likely it is that something will go wrong.

## Slide 9: Options for separating solids from liquids
Limitation on solid concentration
Mobile liquid rather than pellet
Disc-stack centrifuge
Decanter centrifuge
Filtration
Higher solids handling capability
Lower g-force than disc-stack
Rotating drum or belt
Membrane filtration (micro or ultra)
Notes: Most processes involve at least one solid-liquid separation step and whilst bucket centrifuges are used at laboratory scale, at plant scale it is normal to use continuous flow systems of which there are several variations. In contrast to bucket centrifuges which produce a solid pellet, continuous flow disc-stack centrifuges produce a mobile cream with a maximum dry weight concentration of approximately 100 grams per litre which constrains subsequent processing options. An alternative is a scroll-decanter centrifuge which can handle higher solids concentrations but is less efficient at clarifying, especially with smaller particles due to lower centrifugal force than disc-stack.
Depending on the nature of the microorganism and the location of the product (intra- or extracellular) filtration may be a good alternative to centrifugation. A variety of filtration systems exist, for example rotating drum or belt filters fitted with a fabric filter cloth, these can be used with a filter aid if required. Membrane filtration systems of various types are also available, and the porosity of the membrane can be chosen to suit the task (cell removal, soluble protein fractionation according to molecular mass). These systems typically operate with the flow of material being filtered passing tangentially across the face of the membrane to minimise the risk of blocking the membrane pores – tangential flow filtration (TFF).
Image credits:
Disc-stack centrifuge and membrane filtration images are CPI owned
Decanter centrifuge
https://commons.wikimedia.org/wiki/File:Horizontal_Decanter_Centrifuge.png

## Slide 10: Cell-free extracts
Direct from fermenter
Flocculation of nucleic acids & cell wall debris
Continuous-flow high pressure homogenisation
Dialysis
Makes clarification easier
Centrifugation or filtration
Not possible at scale
Use diafiltration instead
Notes: Where intracellular products are the target, a key operation is cell homogenisation. This is usually carried out using continuous flow high pressure homogenisers which typically operate at pressures in excess of 1000 bar. Often multiple passes through the homogeniser are required to maximise cell breakage. This process generates significant heat which must be carefully controlled if the product is heat labile. Given the large volumes involved, long processing times and the limited concentration that can be achieved with continuous flow centrifuges it is common practice to send the cell broth direct from the fermenter to the homogeniser.
The relatively low centrifugal force produced by continuous flow centrifuges means that clarification of homogenates often requires the use of polyethlene imine (PEI) to flocculate the nucleic acids and cell wall debris prior to centrifugation and improve the subsequent solid-liquid separation. PEI treated extracts can also be clarified by filtration.
Dialysis, although commonly used at laboratory scale, cannot be applied at large scale. Instead diafiltration is used, where the extract is concentrated using a membrane filtration device with the appropriate molecular mass selectivity. The concentrate is then diluted with the appropriate buffer and re-concentrated multiple times until the appropriate buffer composition is achieved.
Image credits:
CPI owned

## Slide 11
  Solids
    Various drying modes
  Non-volatile solutes
    Spray drying (heat-stable products)
    Freeze drying
    Resin capture/elution in batch mode
    Solvent extraction
    Crystallisation
Product recovery
Notes: Product recovery is a critical part of any manufacturing process but during the early stages of development focus is often on analysis of product concentration in-situ with little consideration of how the product might be recovered for commercial use. The recovery approach taken will be dictated by the physical properties of the target compound.
The processing of insoluble solids such as biomass is typically by centrifugation or filtration, usually followed by a drying process using hot air in one of several different modes.
Recovery of non-volatile solutes can be by spray drying, a high throughput and relatively cheap process, however this may not be suitable for heat labile products due to the high temperatures involved. Freeze drying offers a more gentle approach but is much more expensive and more challenging for large volume products
The capture of solutes from solution using an absorbent resin can be a useful way of recovering products and offers the opportunity to concentrate and increase product purity.
For more hydrophobic compounds, organic solvent extraction is a useful approach, but care needs to be taken to avoid formation of stable emulsions, centrifugal extractors are a good solution to this problem.

## Slide 12: Purification
Is purification necessary?
Chromatography used only in exceptional circumstances
Resin-binding in batch mode is a useful technique
TFF membrane separation replaces size exclusion chromatography
Distillation & crystallisation
crude
purified
Notes: Purification can contribute significantly to the overall cost of a process so a critical decision is whether purification is actually needed and if so to what level, this will be product and application specific.
Despite routine use at laboratory scale, chromatography is used only in exceptional circumstances at plant scale and the routine use of His-tagged protein purification using metal affinity resins is not common practice. This feeds back to the selection of expression systems, no point in tagging a protein if the tag won’t be used.
Resins can be useful in recovering and purifying proteins and metabolites from solution, but the mode of operation is usually batch. In this approach the resin (ion exchange, hydrophobic etc) would be added to the liquor under conditions designed to bind the target product. After equilibration the resin would typically be drained, washed and then the product eluted. These operations can be carried out in an agitated filter-drier.
Whereas in the laboratory, purification of molecules on the basis of molecular mass would typically be by size exclusion chromatography, on large scale this can be replaced by the use of TFF. SEC is impractical at scale due to the quantities of product that can be separated (low product weight to column volume) and the compressibility of SEC resins in tall columns.
Crystallisation or distillation can be used depending on the physical characteristics of the product.

## Slide 13: Formulation is important to ensure your product is:
Stable to storage
01
Usable by end-user
03
02
Easily transportable
Notes: Product formulation is another important consideration but is often neglected by those inexperienced in large scale operations until late in process development.
Stability is a critical consideration; what is the shelf-life under different storage conditions? In the laboratory, storage at -20 ⁰C or even in liquid nitrogen is not uncommon but these approaches are impractical for bulk products. Ideally the product should be stable at ambient temperature.
Whether a product should be formulated as a dry solid or as a solution will vary by product and application, there is no single, optimum form. For example, solid products are cheaper to transport and take up less storage space than solutions, however, if the product is a protein with potential for sensitisation of end users, then formulation as a solution reduces the risk of exposure via dust inhalation. An alternative would be to granulate the product to reduce the risk of dust generation. These are important considerations and can require significant experimental testing and development and could cause a project to fail after significant effort and money has been invested if not considered early in the process development.

## Slide 14: Logistics to consider
Process timings
Large volumes of aqueous waste
May require off-site treatment
Safety
Loss of containment
Contamination of personnel and environment
Do you require HSE or other authorisation?
Regulations
Everything takes longer
Stability of products during processing
Cooling can take hours
Freezing is costly and impractical
Waste
Notes: Everything takes longer on plant than it does in the laboratory and this needs to be considered when developing a process. Whereas a reaction can be halted in the laboratory in a matter of seconds by immersing a reaction tube in liquid nitrogen, it can take many hours to reduce the temperature of a large- scale reactor by as little as 10 ⁰C. Cell separation may be achieved in as little as 2-3 minutes in a microfuge but would take hours in a disc-stack centrifuge and still not provide a solid pellet.
Waste disposal needs to be carefully planned. Can the waste be sent directly to the waste-water treatment plant or does it require any pre-treatment? Will it need specialist off-site treatment requiring transport by tanker? Are there any solid wastes for disposal by landfill? If so testing may be required to confirm environmental safety.
Are there any non-standard safety issues to consider?
Are there any authorisations required before manufacture, for example HSE or local authority?

## Slide 15: Summary
What is possible at scale?
Not just about the science
Careful planning is essential
Optimise under full-scale conditions
Scale-down approach
Quantifies potential of process at scale
Reduced risk of failure (technical and economic)
Cost based on plant-occupancy
High volumetric productivity is a key target
Low concentrations destroy economics
Notes: Scaling up processes requires skills and experience that the average laboratory researcher is unlikely to possess. To ensure the best chance of success it is vital to collaborate at the earliest opportunity with experts in process scale-up.
Keep things as simple as possible to maximise process robustness, if it doesn’t add robustness and/or yield, don’t do it.
The scale-down approach will give a better understanding of how the process will operate at scale, this permits more accurate economic predictions to be made based on real-world operating conditions before any significant investment is needed for scale-up. Scale-down also enables more experiments to be carried out at lower cost giving vital information on reproducibility and robustness of the process; the manufacturing plant is not the place to be discovering weaknesses in your process. Simplicity and robustness tend to go together.

## Slide 16: Any questions?
Bob Holt

## Slide 17: Icons for activities