## Slide 1: Extraction, Reaction and Other
Endless possibilities
Lead/facilitator name

## Slide 2: Session 6 – Processing 2
Endless possibilities
2
Stirred tanks
Extraction
Thermochemical processing
1
4
3
Novel reactors
5
Notes: Microsoft image to represent conversion/transformation

## Slide 3: Endless Possibilities
Food supply chain residues
sugars
phenols
collagen
starch
natural dyes
chitosan
cellulose
pectin
hemicellulose
waxes
films
bio-adhesives
hydrogels
natural chelants
bio-solvents
chemical monomers
nanocomposites
bio-surfactants
PVC replacements
liquid fuels
cosmetic waxes
solid fuels
hydrophobes
lignin
Notes: PepsiCo looks to reuse plant waste Mar 14, 2011 6:10pm EDT CHICAGO (Reuters) - PepsiCo Inc (PEP.N) is working on ways to reuse waste like oat husksand orange peels, to save money in its supply chain, in areas such as packaging.

## Slide 4
Biomass
Biopolymers
Chitin/chitosan
Starch
Secondary metabolites
Essential oils
Protein
Oil/Fat
Waxes
Sucrose
Cellulose
Hemicellulose
Lignin
Pharmaceuticals
Antioxidants
Pigments
Notes: Quick show of hands, does anyone’s process fit into here?

## Slide 5
Notes: Image source Top Value Added Chemicals from Biomass, Volume 1 – Results of Screening for Potential Candidates from Sugar and Synthesis Gas http://www.eere.energy.gov

## Slide 6: What do you know of large scale reactors? Have you looked at options for your process?
Share with the group
2 mins

## Slide 7: Stirred Tank Reactors: The Go-To Reactor
Classic, scalable and understood
Range of reactor sizes
Well characterised or able to model heat transfer & cooling
Stirring and baffles
Generally as flexible as round bottom
Continuous vs batch
Material compatibility
Catalysts & enzymes
Heating & cooling times
Reaction calorimetry & safety
Integrated DSP
Notes: Classic, scalable and understood
Range of reactor sizes available – width, height, surface/volume ratio options
Well characterised or able to model heat transfer & cooling
Stirring and baffles - limitations with high solids & viscosity
Generally as flexible as round bottom flask – pressure, drain/addition, temperature, distillation
Continuous vs batch
Material compatibility – stainless steel standard, glass lined metal, hastalloy, plastic lined metal
Catalysts & enzymes - supported or homogeneous – recovery vs activity
Heating & cooling times
Reaction calorimetry & safety – thermal runaway
Integrated DSP – biphasic or reactive distillation

## Slide 8: Extraction
Traditional
Steeping, percolating, continuous counter current (CCC)
Ability to heat, agitation sonication
Toxicity, cost, volatility, reuse/disposal, compatibility with market product
Lab solvents vs industrial solvents
Alternatives
Green solvents
Supercritical CO2
CCC for oils, essential oils
Consider
Solvent ratio is key to scale up
Angels share
Reuse, recycling and waste
Product and solid DSP
Ethanol example
Duties
Industrial denatured

## Slide 9: Do you have any ideas or questions about your solvents?
Share with the group
2 mins

## Slide 10: Supercritical Fluid Extraction
Supercritical fluids have
High diffusivity
Solubility tuneable with pressure and temperature
Supercritical CO2
No residue
Tuneable with co-solvents
Easily achieved; 31 °C, 74 bar
The BDC system:
2 × 5 L extraction vessels
co-solvent pump
3 × 2 L pressurised collection vessels
CO2 recycling

## Slide 11: Thermochemical Processing
Commercial suppliers for plant and material (bio-char/pyrolysis oil exist)
Scale up of heating rate and hold time
Inerting gas vs vacuum vs returned gas
Gas scrubbing / afterburner / thermal oxidiser
Energy recovery
Emissions
By-product - how to capture? Outlet?
  Char cooling/quenching
  Wet product
  Pyrolysis oil
  Use of syngas
  Carbon credits

## Slide 12: Novel Reactors
Chemical
Laboratory microwaves (RF etc), ultrasound (cavitation) – change in technique on scale up. T/P to Energy density.
Electrochemistry – growing, scale out
Microreactors – safety advantages, high energy transfer, low inventory. 3d printers.
Mechanical
High shear mixing – established in food industry.
Extrusion
Mechano-chemistry
Challenges
Energy usage / use of renewables – energy storage?
Commercial suppliers – small number or lack of.
Equipment
Engineers/service network/parts. Tame open-minded engineers or learn in-house.
Warranties/guarantees/manuals
Notes: Additional challenges - double innovation but opportunity for patents
MW / ultrasound – out there but kept low key
Take knowledge from other industries

## Slide 13: Novel Reactors
Chemical
Laboratory microwaves (RF etc)
Ultrasound (cavitation)
Electrochemistry
Microreactors
Mechanical
High shear mixing
Extrusion
Mechano-chemistry
Challenges
Energy use and storage
Small number of commercial suppliers
Equipment
Maintenance (servicing and parts)
Warranties/guarantees/manuals
Notes: Additional challenges - double innovation but opportunity for patents
MW / ultrasound – out there but kept low key
Take knowledge from other industries

## Slide 14: Top Tips
General
Minimum viable product and market want
Second hand reactors
Impact on upstream & downstream
Reproducibility / operating windows
Analysis & in-process checks
Safety
Start small and work up
Corrosion and compatibility
Money
Time vs cost (temperature & pressure = ££)
Plant intensity – downtime and maintenance
Waste vs by-product
Reagent / solvent reuse

## Slide 15: Summary
CSTR
The go-to reactor for chemistry
Extractions
Natural product/oil/etc extraction and recovery – how to move from high yield to high product
Thermochemical processing
High temperature routes to biochar and building blocks
Novel reactor development
Pushing new boundaries

## Slide 16: Any questions?
Mark Gronnow
mark.gronnow@york.ac.uk